## Slide 1: The LDT-AIR Project
Derek Clark (PSE)
Josh Jordan (PSE)
Ken Figueiredo (CpE)

## Slide 2: Motivation
To have a secure channel to transfer data
Rugged and reliable.
Send data over land that you don’t own.
Immune to Electromagnetic interference.
Cheaper hassle-free alternative conventional wire/fiber.

## Slide 3: Requirements & Goals
Requirements:
  At least a 1Mbps connection speed with less than a 15% error rate.
  Be able to create a connection over a distance of 15 feet.
Goals:
  Reach a transfer speed on par with Wi-Fi (54Mbps – 600Mbps)
  Be able to create a connection greater than 2 miles.
  A bit error rate of zero.

## Slide 4: Project Specifications
Speeds comparable to Wi-Fi (54Mbps).
Transmit and receive data >15ft.
Send text messages, files, music and video.

## Slide 5: Block Diagram

## Slide 6: Transmitter Housing

## Slide 7: Fiber Pigtail
Single Mode Fiber | Multi-Mode Fiber
Expensive | Less expensive
Smaller Numerical Aperture | Larger Numerical Aperture
Lower Dispersion | Higher Dispersion and attenuation

## Slide 8: Laser Fiber Connector
Pigtail laser package comes with FC/PC adapter.
Coupling loss is associated with adapters.
Makes alignment of the system easier.
Allows for troubleshooting. laser is bad.

## Slide 9: Lens Housing

## Slide 10: Lens Type
Plano-convex lens with no AR coating.
Focal length at 25mm.
Designed specifically for 1550nm wavelength.
Associated lens holder was incorporated to make fastening easy.

## Slide 11: Power

## Slide 12: AC/DC Regulator Comparison
 | Supply Current | Seller | Supply Voltage | Number of Adapters | Cost $
NA | 1000mA | Skycraft | 2-12V | 6 plugs | $9.99
Original Power Powerline | 1300mA | Walmart | 3-12V | 7 Plugs | $11.65
Velleman PSSMV1USA | 1500mA | Amazon | 3-12V | 8 Plugs | $14.99
Enercell | 1000mA | Radioshack | 3-12V | 0 Plugs | $19.99

## Slide 13: 3.3V Regulator Comparison
 | Components | Bill of Materials Cost | Efficiency | Frequency | Temperature
TPS62122 | 7 | $0.68 | 72% | 874kHz | 35°C
TPS62120 | 8 | $0.69 | 72% | 874kHz | 35°C
TPS563200 | 7 | $0.89 | 84% | 78kHz | 31°C

## Slide 14: 3.3V Regulator Circuit

## Slide 15: 3.3V Regulator Prototype

## Slide 16: 5V Regulator Comparison
 | Components | Bill of materials | Efficiency | BOD Footprint
TSP62153 | 6 | $1.17 | 94% | 80
TPS562209 | 8 | $0.82 | 94% | 112
TPS563209 | 8 | $1.37 | 95% | 116
TSP62153

## Slide 17: 5V Regulator Circuit

## Slide 18: 5V Regulator Prototype

## Slide 19: USB vs Ethernet
USB:
  Easier to Implement
  Heavily researched
  Up to 600 Mbps with USB 3.0
Ethernet:
  More difficult to implement
  Heavily researched
  Up to 1Gbps with 10/100/1000

## Slide 20: STM32F405RG
Operating Voltage: 1.8V - 3.6V
ARM 32bit Cortex – M4 core
Pros:
    168 MHz clock speed
    Has an onboard DAC
    Data rate to PC has up to high speed USB 2.0 (480Mbps)
Cons:
  None so far.
10mm
10mm

## Slide 21: Atmega2560
Operating Voltage 1.8V – 5.5V
Pros:
    16MHz clock speed
    Has an onboard DAC
Cons:
  Data rate to PC limited to 2Mbps

## Slide 22: FPGA vs MCU
FPGA:
  Parallel computation
  High speed potential
  Expensive
  No embedded flash memory
MCU:
  Highly researched
  Limited speed
  More support
  No embedded flash memory

## Slide 23: Transmitter code structure
Notes: Here you can see the class diagram of how the transmitter side PCB will receive input from the PC.
We will take the user input in a String, encode into a packet with a header, with a packet ID.
Once the data has been encoded we will pass that data to the MCU to pulse the laser.

## Slide 24: Receiver code structure

## Slide 25: Error handling
Packet Loss
Signal Interference

## Slide 26: Original MCU Schematic

## Slide 27: Original MCU UART

## Slide 28: Laser Wavelength
Selected 1550nm wavelength.
Standard in Telecommunication.
Safe operating wavelength.
Sunlight spectrum will not interfere with the photodetector.

## Slide 29: Laser Comparison
 | Wavelength Range (nm) | Operating Voltage (V) | Threshold Current (mA) | Output Power CW (mW) | Pulse Width (ns) | Price $
Diode Only Quantum Well Laser |  |  |  |  |  | 
Panasonic LNCT28PF01WW | 656-665 | 2.4 | 50 | 100 | 30 | 15.62
Panasonic LNCT22PK01WW | 777-791 | 2.5 | 45 | 200 | 100 | 15.62
Diode Only Vertical Cavity Surface Emitting Laser |  |  |  |  |  | 
TT Electronics OPV300 | 860 | 2.2 | 3 | 1.5 | .2 | 14.65
TT Electronics OPV314AT | 860 | 2.2 | 3 | .6 | .210 | 20.50
Pigtail Package Quantum Well Laser |  |  |  |  |  | 
US-Lasers MM850-0 | 840-860 | 2.4 | 20 | 5 | - | 76.0
Renesas NX7338BF-AA | 1310 | 2.5 | 20 | 10 | 4 | 266.0
Renesas NX7538BF-AA | 1550 | 2.5 | 45 | 10 | 4 | 285.95
14 Pin Butterfly Package Quantum Well Laser |  |  |  |  |  | 
Mitsubishi FU-68SDF-V802M | 1550 | 1.8 | 10 | 6 | .150 | 148.50

## Slide 30: Laser Package
Small, and flexible design.
Circuitry includes built-in Thermoelectric cooler and monitor photodiode.

## Slide 31: Laser Driver Comparison
 | Supply Voltage (V) | Min Bias Current (mA) | Packaging Configuration | Data Rates (Gbps) | Pulse Width (ps) | Price $
Texas Instruments ONET1101L | 3.3 | 5 | QFN Package | 2-11.3 | 60 | Sample
Mindspeed M02067 | 3.3 | 4 | Tray | up to 2.1 | <150 | 8.50
Philips TZA3047A | 3.3 | 5 | BCG | .030-1.25 | 300 | 10
Texas Instruments ONET4201L | 3.3 | 5 | QFN Package | .155-4 | 60 | Sample

## Slide 32: Laser Driver Circuit

## Slide 33: Photodetector
Thorlabs FGA01 ($56.70)
InGaAs material
Wavelength range: 800 - 1700 nm
Responsitivity: 1.003 A/W
NEP@1550nm,20V: 4.5x10^-15W/Hz
Reverse Bias: 20V (max)
Dark Current: 0.05 nA, 2 nA (max)

## Slide 34: Operation Mode
Photovoltaic
  solar cell
Photoconductive
  photodetector

## Slide 35: Photodetector Circuit
Prototype circuit using IR LEDs
2 Mbps max rate
ATMEGA2560
Radioshack parts
($3.99).

## Slide 36: Housing design
Design will be portable.

## Slide 37: Receiver issues
Small active area diameter: 0.12 mm
Beam Dispersion
Atmospheric Absorption

## Slide 38: Accommodations
Ball Lens
0.06” diameter
In door experiments

## Slide 39: Budget
 | Amt. | Cost
Infrared emitter & detector | x1 | $ 9.99
Thorlabs FGA01 | x1 | $ 56.70
Mitsubishi Laser FU-68sdf-v802m | x1 | $ 148.50
opamps | x2 | $3.00
Circuit Board | x1 | $4.00
Inductor Kit | x1 | $ 14.44
Capacitor Kit | x1 | $ 14.00
Laser Driver | x3 | $ 3.57 (free)
Transimpedance Amplifier | x2 | $ 7.85 (free)
Dip Adapter | x3 | $15.00
AC – DC converter | x2 | $10.00
Heat Sink | x1 | $4.95

## Slide 40: Budget Cont.
Coaxial Cable | 12 feet | $2.50
Lens | x1 | $24.30
Lens Housing | x1 | $15.23
Hardware for lens | NA | $5.31
Hardware for Electric circuit | NA | $33.55
2.1mm PowerJack | x1 | $0.75
Lexan Sheet | x1 | $60.00
Brackets/Bolts/Nuts | NA | $6.00
Perforated Circuit Board | x1 | $6.99
STM32F746 Discovery Board | x2 | $100.00
Infrared Card | X1 | $73.00
Total: |  | $624.75
Allotted Budget: |  | $500.00

## Slide 41: Work Distribution
 | Transmitter | Receiver | Microcontroller | Power System
Derek | P | S | S | 
Josh | S | P | S | P
Ken |  |  | P | S

## Slide 42: Future Applications
Temporary network in case of disaster
Satellite / Aircraft communication
LIDAR
Can send data over multiple laser beams to one photodetector.
Temporary network in case of a disaster.

## Slide 43: Successes and Difficulties

## Slide 44
Questions?